## Slide 1: Development and Experimental validation of the Neutron Imaging Capability of the Dual Gamma-Neutron Vision (GN-VISION)
Erasmus Mundus
JMD on Nuclear Physics
G. Cisterna, J. Lerendegui-Marco, J. Balibrea-Correa, I. Ladarescu, C. Domingo-Pardo, B. Gameiro, V. Babiano, J. Hallam
Universidad de Sevilla, Sevilla, España
Instituto de Física Corpuscular,, València, España
University of Surrey, Guildford GU2 7XH, UK

## Slide 2
Background for the development of GN-Vision

## Slide 3: Background Motivations
Hadron Therapy
  Particle therapy
    Enhanced in-vivo range verification
    Improved biological effectiveness of PT
  Boron Neutron Capture Therapy (BNCT)
National Security and Nuclear Energy Industry
  Characterizing spent-fuel from nuclear reactors for decommissioning
  Homeland Security
* Simposio GEFN, XXXVIII Reunión Bienal de la RSEF, July 13th 2022, Murcia
“i-TED: Imaging neutron capture sections & applications”
*IAEA Incident and Trafficking Database (ITDB): 2022 Fact Sheet

## Slide 4: The i-TED Concept
State-of-the-Art and Motivation
  Significantly improve the signal-to-background ratio in neutron capture measurement
  Relevance for the stellar nucleosynthesis in key (n,γ) reactions
i-TED Design
  Scatter PSD plane: 50x50x15mm LaClscintillation crystal
  Absorber PSD plane: 4 50x50x25mm LaCl scintillation crystal
  Each crystal: 8x8 SiPM (6% @ 662 keV and 1-3 mm spatial resolution )
  The full i-TED 1280 output signals
  Integrated SiPM readout system developed by PETsys Electronics: the front-end house ASICs and back-end with FPGA boards
Compton Imaging
Fast Back-Projection (BP)

## Slide 5
GN-Vision: Imaging of -rays and Neutrons

## Slide 6: Overview & Core components of GN-Vision
*Jorge Lerendegui-Marco et al.: “Simultaneous Gamma-Neutron Vision device: a portable and versatile tool for nuclear inspections”
Overview of GN-Vision
  Built upon the technological foundation established by the i-TED system, incorporating significant enhancements :
    Scatter PSD: By replacing the scatter crystal from LaCl to CLYC-6
    Slow Neutron Imaging:passive pinhole collimator
Pinhole Collimator
  Collimator material is due to its high absorbing power and simple mechanization.
  does not emit -rays.
  is 95% purity but natural is under studied for cost reduction reasons
  Neutron image is formed by scaling the interaction positions in the CLYC detector by the ratio between the LongFocal distance and ShortFocal distance
LongFocal
ShortFocal
Neutron Imaging
Compton Imaging

## Slide 7: Overview & Core components of GN-Vision
CLYC crystal:
  (CLYC) monolithic crystals as Scatter PSD:
    Thermal Neutrons: with a cross section of 940 b and = 4.78 MeV (3.2 MeVee)
    To enhance fast neutron detection: instead of .
Neutron-Gamma Discrimination via Pulse Shape Discrimination
Thermal Neutrons
-rays

## Slide 8: Readout electronics of GN-Vision
Challenges with Individual Read-Outs
  Light yield CLYC is 20,000 photons per MeV much smaller than LaCl of 50,000 photons per MeV
  Signal width of CLYC (4-5 µs) is greater and more diffuse than that of LaCl (300 ns)
  Light yield per ns and per MeV in CLYC is 80 times smaller leading to SNR challenges when using CLYC with pixelated SiPMs
Charge Modulation-Based Multiplexing (CMBM)
i-TED

## Slide 9: GN-Vision: status and goals of this work
V
Monolithic crystal + SiPM array
=
Spatial Resolution depending
on pixels activated
Our objectives include:
  Spatial Resolution Characterization
    Spatial resolution of CLYC monolithic crystal using AiT's readout for -radiation.
  Linearity Study
    Linearity of the CLYC crystal of interaction points
  Neutron Response and Discrimination
    Initial tests of GN-Vision's response to neutron irradiation
  Experimental Proof-of-Concept
    Experimental proof-of-concept for neutron imaging capability at ILL, France

## Slide 10
Characterization of the spatial resolution of the CLYC

## Slide 11: Experimental Setup and Measurements
Positioning holes
Collimator hole
22Na Source
Experimental Set up
  2 CLYC scintillator crystal: One located at the top and one at the bottom of the setup.
  8 × 8 silicon photomultiplier array (SiPM) from SensL (ArrayJ-60035-65P-PCB) couple to lower CLYC.
  PMT :couple to upper CLYC
  4-Channel Readout instrumentation from AiT: Readout electronic lower CLYC.
  CAEN DT5730S DAQ motherboard: for data acquisition and processing of signals from the setup.
  Movable platform (T-G-LSM200A200): Mechanical material with a microstep precision of 0.047625 μm, used to move the position-sensitive detector.
  Na source (2 MBq activity): a gamma-ray source in the setup.
  Collimators: Tungsten parallelepiped collimator, circular tungsten collimator and Lead collimator. Distance between the front faces of both CLYC crystals is 26 cm. Provide Mechanical collimation.
X
Z

## Slide 12: Gamma-Ray Event Selection & Interaction Position Reconstruction
Ch 5: CLYC + PMT
Ch 0: CLYC + SiPM
Ch 0: CLYC + SiPM
Coincident and fully absorbed events
Interaction position reconstruction

## Slide 13: Geant4 simulations
Projections of the Geant4 simulation convoluted with a Gaussian distribution with std. dev. 2.25 mm
Comparison of the measured projections with the convoluted projections
Center the collimator hole with the
center of the CLYC crystal: (0x,0y)
—————
Mean: 0.02 0.02 mm
Std. Dev.: 1.48 0.02 mm
—————
Mean: 0.02 0.02 mm
Std. Dev.: 1.48 0.02 mm
FWHM (x=0,y=0)= 5.18 mm

## Slide 14: Results
Results
  FWHM obtained in these measurements is generally below 6 mm (< pixel size ). Indeed, several points have FWHM values below 5 mm.
  Beyond 15 mm, the compression effect becomes more significant, and almost no positions are reconstructed in this area. Need to apply an analytical or Machine-Learning based correction

## Slide 15
First test of the position-sensitive’s response to neutrons

## Slide 16: Experimental setup & Measurements
Experimental setup:
  Cf source: Neutron and -ray source through alpha decay and spontaneous fission
  Polyethylene (PE): Collimator with a slit for thermal neutrons to reach the CLYC detector.
  PE enriched with 95% of slab: Collimator with a slit for thermal neutrons to reach the CLYC detector.
  CLYC crystal, AiT readout electronics and Caen DACQ Motherboard: The same CLYC and electronics readout utilized in the spatial resolution setup.
  Duplication of Signal: Sum channel provided by AiT readout, duplicated for energy resolution and neutron-gamma discrimination.

## Slide 17: Neutron-gamma discrimination with a CLYC
All events
-rays events
Neutron events
All events
-rays events
Neutron events
Optimized PSD & Energy
Optimized Energy

## Slide 18: Measurements & Results
6LiPE with a slit (~5 mm thick)
6LiPE without a slit (background)
6LiPE with a slit (~5 mm thick) after subtracting the background

## Slide 19
First POC experiment of neutron imaging at ILL

## Slide 20: Experimental setup & Measurements
Experimental Set up
  Experimental setup location: placed in air along the neutron beam, 2 meters downstream from FIPPS installation. Suppression the thermal neutron background.
  Neutron beam: thermal spectrum with a Maxwellian distribution around 25 meV.
  CLYC crystal, AiT 4-Channel Readout instrumentation & CAEN DAQ motherboard: same than previous experimental setups.
  Fig. A: reduced version of GN-VISION, including only the subsystem responsible for neutron imaging
  Fig. B: detail of pinhole collimator.
  Fig. C: target centered with the center of the pinhole collimator.
  Fig. D: final arrangement. GN-VISION positioned transversally to the beam direction.
+X
A
B
C
D
  To place neutrons scattering objects in the thermal neutron beam so that they acts as isotropic sources.

## Slide 21: Results
1 cm PE cube centered in the hole of the collimator
8 cmPE cube centered in the hole of the collimator
1 cmPE cube displaced 2 cm downstream
Beam direction
Beam direction
Beam direction

## Slide 22: Neutron source Imaging
Beam direction
+X
+Y
Neutron imaging

## Slide 23: Conclusions
  Comprehensive Study: The GN-Vision device, designed for dual detection and spatial localization of -ray and neutron sources, was thoroughly studied. Core components like the CLYC crystal, pinhole collimator, and Pulse Shape Discrimination (PSD) for neutron-gamma discrimination were examined.
  Spatial Characterization: A scanning table with mechanical collimation and PET coincidences was used to characterize the CLYC-6 detector's spatial resolution, linearity, and compression for -rays. GEANT4 simulations helped separate the intrinsic resolution of the detector from experimental setup influences. They showed how spatial and energy resolution affect image quality. Results showed high spatial resolution below 6 mm and adequate linearity .
  Imaging Quality: GEANT4 simulations of GN-VISION device were carried to analyze how spatial experimental effects impact on Compton and Neutron imaging. The results showed an imaging broadened source distributions and increased background noise, but source positioning remained accurate.
  Neutron-Gamma Discrimination: Effective discrimination was achieved using PSD techniques, with a high Figure of Merit (FOM) of 2.921 indicating good separation between neutron and -ray events.
  Experimental Validation: Initial tests with a Cf source demonstrated the system's ability to distinguish between s and neutron radiation, with clear interaction patterns corresponding to the experimental setup.
  Neutron Imaging Proof-of-Concept: At the ILL in France, GN-Vision successfully distinguished between different neutron source positions and sizes, confirming its neutron imaging capability and potential for detailed spatial neutron detection.

## Slide 24
THANKS

## Slide 25
Supportive Slide

## Slide 26: Content
Background for the development of GN-Vision
  Motivation
  Scintillation Detectors
  The i-TED Concept
GN-Vision: Imaging of -rays and Neutrons
  Overview & Core components of GN-Vision
  Readout electronics of GN-Vision
  GN-Vision: status and goals of this work
Characterization of the spatial resolution of the CLYC
  Experimental Setup and Measurements
  Geant4 simulations
  Results
Impact of the spatial resolution on GN-VISION
  Geant4 simulation
  Results
First test of the position-sensitive’s response to neutrons
  Experimental setup and Measurements
  Neutron-gamma discrimination
  Results
First POC experiment of neutron imaging at ILL
  Experiment at ILL
  Measurements and Results

## Slide 27: Radiation-Matter Interaction & Scintillation Detectors
-Rays
  Photoelectric Effect
  Compton Scattering
  Pair Production
Neutron
  Elastic Scattering
  Inelastic Scattering
  Absorption Reactions
Scintillation Detectors
  Monolithic Crystals & Pixelated Crystals
Photosensors: PMTs and SiPMs
Radiation-Matter Interaction

## Slide 28: GN-Vision: status and goals of this work
Our objectives include:
  Spatial Resolution Characterization
    Spatial resolution of CLYC monolithic crystal using AiT's readout for -radiation.
  Linearity Study
    Linearity of the CLYC crystal of interaction points
  Performance Impact on GN-Vision
    Characterize how spatial resolution and linearity affect the GN-Vision performance.
  Neutron Response and Discrimination
    Initial tests of GN-Vision's response to neutron irradiation
  Experimental Proof-of-Concept
    Experimental proof-of-concept for neutron imaging capability at ILL, France.
Monolithic crystal + SiPM array
=
Spatial Resolution depending
on pixels activated

## Slide 29: Compton and PET filtering events
i-TED-C:
E1
i-TED-A:
E2
E1 + E2 = Eg
E1’ + E2’ = Eg
E’2
E’1
COMPTON
511 keV
𝛽+
EA
511 keV
PET
ED = 511 keV
EA = 511 keV
(25 PET Coincidence lines in total!)